## Slide 1: DMIS OUTPUT FILE - .dmo

## Slide 2: DMIS Output File Description
FILNAM/‘5678_FULL'
DATE =2023/01/18
TIME =10:18:49
UNITS/MM,ANGDEC
$$ NUMBER PART : 12345678
$$ MODEL : AAA
$$ ROUTINE: FULL
$$ REQUEST:2023-01-18-001
$$ PART MEASURE: 12345678
$$ SHIFT:01
$$ TOOL: 01
$$ OPERATOR: PHIL_SMITH
F(S3970DD01)=FEAT/POINT,CART,2542.950,667.880,969.660,-0.056503,$
-0.923746,-0.378815
T(S3970DD01_N)=TOL/PROFS,-0.7500,0.7500
T(S3970DD01_X)=TOL/CORTOL,XAXIS,-0.750,0.750
T(S3970DD01_Y)=TOL/CORTOL,YAXIS,-0.750,0.750
T(S3970DD01_Z)=TOL/CORTOL,ZAXIS,-0.750,0.750
OUTPUT/FA(S3970DD01),TA(S3970DD01_N),TA(S3970DD01_X),TA(S3970DD01_Y),$
TA(S3970DD01_Z)
FA(S3970DD01)=FEAT/POINT,CART,2543.145,668.829,970.017,0.056503,$
0.923746,0.378815
TA(S3970DD01_N)=TOL/PROFS,1.023,1.023,OUTOL
TA(S3970DD01_X)=TOL/CORTOL,XAXIS,0.195,INTOL
TA(S3970DD01_Y)=TOL/CORTOL,YAXIS,0.949,OUTOL
TA(S3970DD01_Z)=TOL/CORTOL,ZAXIS,0.357,INTOL
Measurement Program Information
Sample Header Information
Feature Nominal Information
Feature Actual Measurement Information

## Slide 3: Measurement Program Information
FILNAM/‘5678_FULL'
DATE =2023/01/18
TIME =10:18:49
UNITS/MM,ANGDEC
Filename of the Program that was run to measure the part
Date and Time the sample was measured
Measurement units used
The Measurement Program Information is used to show information about the inspection program. The example shows the name of the inspection program, the date and time the program was run, and the unit of the measurement used for measuring the sample.
Note: This is information on the running of the inspection program, the date and time does not necessarily reflect anything specific to the sample being measured. This Date and Time however is often used and associated with the sample as most manufacturing systems there is not a significant lag between pulling the samples and measuring the samples.

## Slide 4: Header information
$$ NUMBER PART : 12345678
$$ MODEL : AAA
$$ ROUTINE: FULL
$$ REQUEST:2023-01-18-001
$$ PART MEASURE: 12345678
$$ SHIFT:01
$$ TOOL: 01
$$ OPERATOR: PHIL_SMITH
Header lines begin with $$. Header lines are used to hold information about the sample. This information can be things like the part number, shift, tool, or line the part came from. Header lines can also include information about the person running the program. Header lines are customizable and will need to be mapped to fields in QDMWEB. Note: There could be a date and time in this section entered based on the date and time the sample was pulled from production to be measured. In this example there is not, however the part could have been measured during the second shift, but was pulled from the line during the first shift. This would also be a place where a serial number could be entered which could represent production timing.

## Slide 5: Surface Point Measurement
F(S3970DD01)=FEAT/POINT,CART,2542.950,667.880,969.660,-0.056503,$
-0.923746,-0.378815
T(S3970DD01_N)=TOL/PROFS,-0.7500,0.7500
T(S3970DD01_X)=TOL/CORTOL,XAXIS,-0.750,0.750
T(S3970DD01_Y)=TOL/CORTOL,YAXIS,-0.750,0.750
T(S3970DD01_Z)=TOL/CORTOL,ZAXIS,-0.750,0.750
OUTPUT/FA(S3970DD01),TA(S3970DD01_N),TA(S3970DD01_X),TA(S3970DD01_Y),$
TA(S3970DD01_Z)
FA(S3970DD01)=FEAT/POINT,CART,2543.145,668.829,970.017,0.056503,$
0.923746,0.378815
TA(S3970DD01_N)=TOL/PROFS,1.023,1.023,OUTOL
TA(S3970DD01_X)=TOL/CORTOL,XAXIS,0.195,INTOL
TA(S3970DD01_Y)=TOL/CORTOL,YAXIS,0.949,OUTOL
TA(S3970DD01_Z)=TOL/CORTOL,ZAXIS,0.357,INTOL
Nominal information is shown with lines starting with F and T for Feature and Tolerance respectively. F(FeatName)=FEAT/POINT, CART, X, Y, Z, i, j, k
T(FeatName_N)=TOL/PROFS, TolLwr, TolUpr
T(FeatName_X)=TOL/CORTOL, XAXIS, TolLwr, TolUpr
T(FeatName_Y)=TOL/CORTOL, YAXIS, TolLwr, TolUpr
T(FeatName_Z)=TOL/CORTOL, ZAXIS, TolLwr, TolUpr
Actual Measured information is shown with lines starting with FA and TA for Feature Actual and Tolerance Actual respectively. FA(FeatName)=FEAT/POINT, CART, X, Y, Z, i, j, k
TA(FeatName_N)=TOL/PROFS, Actual, Deviation, OUTOL/INTOL
TA(FeatName_X)=TOL/CORTOL, XAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Y)=TOL/CORTOL, YAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Z)=TOL/CORTOL, ZAXIS, Deviation, OUTOL/INTOL
~|1.5|A|B|C

## Slide 6: Rounded Slot Measurement
F(L4032M001)=FEAT/CPARLN,INNER,ROUND,CART,3124.790,569.360,761.160,$
-0.000,1.000,-0.000,1.000,0.000,0.000,18.300,12.300
T(L4032M001_WIDTH_LONG)=TOL/WIDTH,-0.600,0.600,LONG
T(L4032M001_WIDTH_SHORT)=TOL/WIDTH,-0.600,0.600,SHORT
T(L4032M001_X)=TOL/CORTOL,XAXIS,-0.600,0.600
T(L4032M001_Y)=TOL/CORTOL,YAXIS,-0.600,0.600
T(L4032M001_Z)=TOL/CORTOL,ZAXIS,-0.600,0.600
OUTPUT/FA(L4032M001),TA(L4032M001_WIDTH_LONG),$
TA(L4032M001_WIDTH_SHORT),TA(L4032M001_X),TA(L4032M001_Y),$
TA(L4032M001_Z)
FA(L4032M001)=FEAT/CPARLN,INNER,ROUND,CART,3124.778,568.575,760.517,$
0.005,1.000,-0.010,0.998,-0.006,-0.064,20.291,12.501
TA(L4032M001_WIDTH_LONG)=TOL/WIDTH,1.991,OUTOL,LONG
TA(L4032M001_WIDTH_SHORT)=TOL/WIDTH,0.201,INTOL,SHORT
TA(L4032M001_X)=TOL/CORTOL,XAXIS,-0.012,INTOL
TA(L4032M001_Y)=TOL/CORTOL,YAXIS,-0.785,OUTOL
TA(L4032M001_Z)=TOL/CORTOL,ZAXIS,-0.643,OUTOL
Nominal information is shown with lines starting with F and T for Feature and Tolerance respectively. F(FeatName)=FEAT/CPARLN, INNER, ROUND, CART, X, Y, Z, i, j, k
T(FeatName_WIDTH_LONG)=TOL/WIDTH, TolLwr, TolUpr, LONG
T(FeatName_WIDTH_SHORT)=TOL/WIDTH, TolLwr, TolUpr, SHORT
T(FeatName_X)=TOL/CORTOL, XAXIS, TolLwr, TolUpr
T(FeatName_Y)=TOL/CORTOL, YAXIS, TolLwr, TolUpr
T(FeatName_Z)=TOL/CORTOL, ZAXIS, TolLwr, TolUpr
Actual Measured information is shown with lines starting with FA and TA for Feature Actual and Tolerance Actual respectively. FA(FeatName)=FEAT/CPARLN, INNER, ROUND, CART, X, Y, Z, i, j, k
TA(FeatName_WIDTH_LONG)=TOL/WIDTH, Deviation, OUTOL/INTOL, LONG
TA(FeatName_WIDTH_SHORT)=TOL/WIDTH, Deviation, OUTOL/INTOL, SHORT
TA(FeatName_X)=TOL/CORTOL, XAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Y)=TOL/CORTOL, YAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Z)=TOL/CORTOL, ZAXIS, Deviation, OUTOL/INTOL
#|1.2|A|B|C
6±0.6 X 12±0.6

## Slide 7: Rectangular Slot
F(M3970M006)=FEAT/CPARLN,INNER,FLAT,CART,2323.000,579.750,1073.000,$
0.000,0.985,0.174,1.000,-0.000,0.000,17.754,12.137
T(M3970M006_WIDTH_LONG)=TOL/WIDTH,-0.500,0.500,LONG
T(M3970M006_WIDTH_SHORT)=TOL/WIDTH,-0.500,0.500,SHORT
T(M3970M006_X)=TOL/CORTOL,XAXIS,-0.500,0.500
T(M3970M006_Y)=TOL/CORTOL,YAXIS,-0.500,0.500
T(M3970M006_Z)=TOL/CORTOL,ZAXIS,-0.500,0.500
OUTPUT/FA(M3970M006),TA(M3970M006_WIDTH_LONG),$
TA(M3970M006_WIDTH_SHORT),TA(M3970M006_X),TA(M3970M006_Y),$
TA(M3970M006_Z)
FA(M3970M006)=FEAT/CPARLN,INNER,FLAT,CART,2323.516,579.226,1072.839,$
-0.007,0.985,0.175,1.000,0.008,-0.004,18.841,13.323
TA(M3970M006_WIDTH_LONG)=TOL/WIDTH,1.087,OUTOL,LONG
TA(M3970M006_WIDTH_SHORT)=TOL/WIDTH,1.186,OUTOL,SHORT
TA(M3970M006_X)=TOL/CORTOL,XAXIS,0.516,OUTOL
TA(M3970M006_Y)=TOL/CORTOL,YAXIS,-0.524,OUTOL
TA(M3970M006_Z)=TOL/CORTOL,ZAXIS,-0.161,INTOL
Nominal information is shown with lines starting with F and T for Feature and Tolerance respectively. F(FeatName)=FEAT/CPARLN, INNER, FLAT, CART, X, Y, Z, i, j, k
T(FeatName_WIDTH_LONG)=TOL/WIDTH, TolLwr, TolUpr, LONG
T(FeatName_WIDTH_SHORT)=TOL/WIDTH, TolLwr, TolUpr, SHORT
T(FeatName_X)=TOL/CORTOL, XAXIS, TolLwr, TolUpr
T(FeatName_Y)=TOL/CORTOL, YAXIS, TolLwr, TolUpr
T(FeatName_Z)=TOL/CORTOL, ZAXIS, TolLwr, TolUpr
Actual Measured information is shown with lines starting with FA and TA for Feature Actual and Tolerance Actual respectively. FA(FeatName)= FEAT/CPARLN, INNER, FLAT, CART, X, Y, Z, i, j, k
TA(FeatName_WIDTH_LONG)=TOL/WIDTH, Deviation, OUTOL/INTOL, LONG
TA(FeatName_WIDTH_SHORT)=TOL/WIDTH, Deviation, OUTOL/INTOL, SHORT
TA(FeatName_X)=TOL/CORTOL, XAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Y)=TOL/CORTOL, YAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Z)=TOL/CORTOL, ZAXIS, Deviation, OUTOL/INTOL
#|1.2|A|B|C
6±0.5 X 12±0.5

## Slide 8: Round Hole
F(H8566DB01)=FEAT/CIRCLE,INNER,CART,2737.369,869.000,581.050,0.000,$
1.000,-0.000,8.199
T(H8566DB01_DIAM)=TOL/DIAM,-1.000,1.000
T(H8566DB01_X)=TOL/CORTOL,XAXIS,-1.000,1.000
T(H8566DB01_Y)=TOL/CORTOL,YAXIS,-1.000,1.000
T(H8566DB01_Z)=TOL/CORTOL,ZAXIS,-1.000,1.000
OUTPUT/FA(H8566DB01),TA(H8566DB01_DIAM),TA(H8566DB01_X),$
TA(H8566DB01_Y),TA(H8566DB01_Z)
FA(H8566DB01)=FEAT/CIRCLE,INNER,CART,2737.178,867.988,580.979,-0.005,$
1.000,0.010,8.258
TA(H8566DB01_DIAM)=TOL/DIAM,0.059,INTOL
TA(H8566DB01_X)=TOL/CORTOL,XAXIS,-0.191,INTOL
TA(H8566DB01_Y)=TOL/CORTOL,YAXIS,-1.012,OUTOL
TA(H8566DB01_Z)=TOL/CORTOL,ZAXIS,-0.071,INTOL
Nominal information is shown with lines starting with F and T for Feature and Tolerance respectively. F(FeatName)=FEAT/CIRCLE, INNER, CART, X, Y, Z, i, j, k
T(FeatName_DIAM)= TOL/DIAM, TolLwr, TolUpr
T(FeatName_X)=TOL/CORTOL, XAXIS, TolLwr, TolUpr
T(FeatName_Y)=TOL/CORTOL, YAXIS, TolLwr, TolUpr
T(FeatName_Z)=TOL/CORTOL, ZAXIS, TolLwr, TolUpr
Actual Measured information is shown with lines starting with FA and TA for Feature Actual and Tolerance Actual respectively. FA(FeatName)= FEAT/CIRCLE, INNER, CART, X, Y, Z, i, j, k
TA(FeatName_DIAM)=TOL/DIAM, Deviation, OUTOL/INTOL
TA(FeatName_X)=TOL/CORTOL, XAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Y)=TOL/CORTOL, YAXIS, Deviation, OUTOL/INTOL
TA(FeatName_Z)=TOL/CORTOL, ZAXIS, Deviation, OUTOL/INTOL
#|:2|A|B|C
:6±1

## Slide 9: Round Pin
F(K8566DB01)=FEAT/CIRCLE, OUTER,CART,2737.369,869.000,581.050,0.000,$
1.000,-0.000,8.199
T(K8566DB01_DIAM)=TOL/DIAM,-1.000,1.000
T(K8566DB01_X)=TOL/CORTOL,XAXIS,-1.000,1.000
T(K8566DB01_Y)=TOL/CORTOL,YAXIS,-1.000,1.000
T(K8566DB01_Z)=TOL/CORTOL,ZAXIS,-1.000,1.000
OUTPUT/FA(K8566DB01),TA(K8566DB01_DIAM),TA(K8566DB01_X),$
TA(K8566DB01_Y),TA(K8566DB01_Z)
FA(K8566DB01)=FEAT/CIRCLE,OUTER,CART,2737.178,867.988,580.979,-0.005,$
1.000,0.010,8.258
TA(K8566DB01_DIAM)=TOL/DIAM,0.059,INTOL
TA(K8566DB01_X)=TOL/CORTOL,XAXIS,-0.191,INTOL
TA(K8566DB01_Y)=TOL/CORTOL,YAXIS,-1.012,OUTOL
TA(K8566DB01_Z)=TOL/CORTOL,ZAXIS,-0.071,INTOL
Nominal information is shown with lines starting with F and T for Feature and Tolerance respectively. F(FeatName)=FEAT/CIRCLE, OUTER, CART, X, Y, Z, i, j, k
T(FeatName_DIAM)= TOL/DIAM, TolLwr, TolUpr
T(FeatName_X)=TOL/CORTOL, XAXIS, TolLwr, TolUpr
T(FeatName_Y)=TOL/CORTOL, YAXIS, TolLwr, TolUpr
T(FeatName_Z)=TOL/CORTOL, ZAXIS, TolLwr, TolUpr
Actual Measured information is shown with lines starting with FA and TA for Feature Actual and Tolerance Actual respectively. FA(FeatName)= FEAT/CIRCLE, OUTER, CART, X, Y, Z, i, j, k
TA(FeatName_DIAM)=TOL/DIAM, Actual, OUTOL/INTOL
TA(FeatName_X)=TOL/CORTOL, XAXIS, Actual, OUTOL/INTOL
TA(FeatName_Y)=TOL/CORTOL, YAXIS, Actual, OUTOL/INTOL
TA(FeatName_Z)=TOL/CORTOL, ZAXIS, Actual, OUTOL/INTOL
#|:2|A|B|C
:6±1